HY330 – Telecommunication Systems
Chris Papastamos | csd4569
Assignment 4

Exercise 1
For the purpose of this exercise I created the following flowgraph:

Lets execute and observe the different outputs produced when changing the two sliders:

Starting up we can see the three signals aligned. This is expected as no modifications have been applied.

After adding some noise, we can observe additional “noise” frequencies in the signal with the added noise.
By changing the second signal’s frequency, the multiplication’s output is the sum of the two frequencies. That is the definition of CFO, The specified value is the Frequency Offset from the Carrier frequency.

Exercise 2
The requested flowgraph for this exercise is the following:
Lets execute and take a look at the output:

Initially, the red signals constellation points align with the reference points since no noise is introduced to the signal.

After adding some noise we can see the signal being spread around the reference points.

Exercise 3
By executing the given flowgraph we observe the following output:

We can see the output signal aligns with the reference constellation points. That is because there is no noise and no CFO. Lets add some:

We can see that even with a small amount of noise and CFO the signal goes away a lot from its original constellation points. Lets try pumping up the variables a little bit more:

With such high amounts of noise and CFO the output signal is completely ruined. Playing some more with the noise and CFO variables, we can see that noise controls the spread of the points and the CFO controls the circular movement of the points around the center point

In order to convert the flowgraph to display QPSK I have to make 2 changes. The first is the number of bytes per constellation point by changing the mod_order variable to 2 bits. The second change is to change the actual constellation points by changing the constellation variable. The new constellation points will be: -1-1j, -1+1j, +1-1j, +1+1j. The final flowgraph looks like this:

The output of the flowgraph is the following:

We can see that the four constellation points appear in the desired locations according to the QPSK specification. Lets add some noise and CFO:

We can observe here the spread and the offset as expected!

To display the 16QAM system we will again change the mod_order to 4bits and constellation according to the new points. The new points are going to be: -3-3j, -1-3j, +3-3j, +1-3j, -3-1j, -1-1j, +3-1j, +1-1j, -3+3j, -1+3j, +3+3j, +1+3j, -3+1j, -1+1j, +3+1j, +1+1j
The output of this system is the following:

Finally for the 64QAM system the mod_order is going to be 6bits and the constellation points will be changed to match (I am not going to include the list because of its size). The output of the system is the following:

In order to normalize the constellation points of each system, I am going to multiply each signal with their system’s respective normalization factor. The updated flowgraph is going to look like this:

The new output of each system is going to be the following:

Lets now look at how much noise each system can handle without having errors:

Lets now look at how much noise each system can handle without having errors: