HY330 – Telecommunication Systems
Chris Papastamos | csd4569
Assignment 5

Exercise 1
For the purpose of this exercise I created the following flowgraph:

This flowgraph modulates the output of the random source (1,-1) with Amplitude Modulation. It uses the variable modulation index to distance the two amplitude modulation points. The output of the flowgraph looks like this:

We can see that the signal has the two amplitude modulation points at 0.2 and at 1.8 ( 1+-0.8 ).

For the shaping of the signal, we can add a Root Raised Cosine Filter to shape our signal. The unshaped and shaped output can be seen below:

Exercise 2
For the 2nd exercise I edited the simplified_fsk.grc by applying the following modifications: I altered the samp rate to 192kSPS and changed the symbol duration to 160 points in order to achieve a bitrate of 1200SPS. The final flowgraph is the following:

In order to shape the output of the signal I used the Root Raised Cosine Filter block. I also used the Frequency Mod block to apply FM to the signal. The output of the flowgraph is the following:

By raising the Frequency Mod sensitivity, we observe the following output:

Exercise 2
In this exercise I had to create a new block called constellation_mapping_4569. For this I used gr-modtool to create a new module (called “chris_module”) and then I created the constellation_mapping_4569 block.

For the purpose of demonstrating the new block I created the following flowgraph:

Next up we can see a screenshot of a run for each value of bitsPbyte [1, 2, 4, 3 (or any other value)]:

   BPSK (1 bitPB)

QPSK (2 bitsPB)

   QPSK (4 bitsPB)

Error Case (3 bitsPB)

The block files are the following and the changes are highlighted:

id: chris_module_constellation_mapping_4569 / label: constellation_mapping_4569 / category: '[chris_module]' / templates: / imports: from gnuradio import chris_module / make: chris_module.constellation_mapping_4569(${mod_bits_cnt}) / # Make one 'parameters' list entry for every parameter you want settable from the GUI. / # Keys include: / # * id (makes the value accessible as keyname, e.g. in the make entry) / # * label (label shown in the GUI) / # * dtype (e.g. int, float, complex, byte, short, xxx_vector, ...) / # * default / parameters: / - id: mod_bits_cnt / label: Modulation bits count / dtype: int / default: 1 / # Make one 'inputs' list entry per input and one 'outputs' list entry per output. / # Keys include: / # * label (an identifier for the GUI) / # * domain (optional - stream or message. Default is stream) / # * dtype (e.g. int, float, complex, byte, short, xxx_vector, ...) / # * vlen (optional - data stream vector length. Default is 1) / # * optional (optional - set to 1 for optional inputs. Default is 0) / inputs: / - label: in / domain: stream / dtype: byte / outputs: / - label: out / domain: stream / dtype: complex / # 'file_format' specifies the version of the GRC yml format used in the file / # and should usually not be changed. / file_format: 1

/* -*- c++ -*- */ / /* / * Copyright 2023 gr-chris_module author. / * / * SPDX-License-Identifier: GPL-3.0-or-later / */ / #ifndef INCLUDED_CHRIS_MODULE_CONSTELLATION_MAPPING_4569_IMPL_H / #define INCLUDED_CHRIS_MODULE_CONSTELLATION_MAPPING_4569_IMPL_H / #include <gnuradio/chris_module/constellation_mapping_4569.h> / namespace gr { / namespace chris_module { / class constellation_mapping_4569_impl : public constellation_mapping_4569 / { / private: / int _mod_bits_cnt; / public: / constellation_mapping_4569_impl(int mod_bits_cnt); / ~constellation_mapping_4569_impl(); / // Where all the action really happens / int work( / int noutput_items, / gr_vector_const_void_star &input_items, / gr_vector_void_star &output_items / ); / }; / } // namespace chris_module / } // namespace gr / #endif /* INCLUDED_CHRIS_MODULE_CONSTELLATION_MAPPING_4569_IMPL_H */

/* -*- c++ -*- */ / /* / * Copyright 2023 gr-chris_module author. / * / * SPDX-License-Identifier: GPL-3.0-or-later / */ / #include <gnuradio/io_signature.h> / #include "constellation_mapping_4569_impl.h" / namespace gr { / namespace chris_module { / using input_type = char; / using output_type = gr_complex; / constellation_mapping_4569::sptr / constellation_mapping_4569::make(int mod_bits_cnt) / { / return gnuradio::make_block_sptr<constellation_mapping_4569_impl>( / mod_bits_cnt); / } / /* / * The private constructor / */ / constellation_mapping_4569_impl::constellation_mapping_4569_impl(int mod_bits_cnt) / : gr::sync_block("constellation_mapping_4569", / gr::io_signature::make(1, 1, sizeof(input_type)), / gr::io_signature::make(1, 1, sizeof(output_type))) / { / _mod_bits_cnt = mod_bits_cnt; / } / gr_complex const_BPSK(char input_bit){ / if(input_bit == 0){ / return gr_complex(1,0); / }else if(input_bit == 1){ / return gr_complex(-1,0); / }else{ / return gr_complex(0,0); / } / } / gr_complex const_QPSK(char input_bit){ / if(input_bit == 0){ / return gr_complex(1,1); / }else if(input_bit == 1){ / return gr_complex(-1,1); / }else if(input_bit == 2){ / return gr_complex(1,-1); / }else if(input_bit == 3){ / return gr_complex(-1,-1); / }else{ / return gr_complex(0,0); / } / } / gr_complex const_16QAM(char input_bit){ / if(input_bit == 0){ / return gr_complex(3,3); / }else if(input_bit == 1){ / return gr_complex(1,3); / }else if(input_bit == 2){ / return gr_complex(-1,3); / }else if(input_bit == 3){ / return gr_complex(-3,3); / }else if(input_bit == 4){ / return gr_complex(3,1); / }else if(input_bit == 5){ / return gr_complex(1,1); / }else if(input_bit == 6){ / return gr_complex(-1,1); / }else if(input_bit == 7){ / return gr_complex(-3,1); / }else if(input_bit == 8){ / return gr_complex(3,-1); / }else if(input_bit == 9){ / return gr_complex(1,-1); / }else if(input_bit == 10){ / return gr_complex(-1,-1); / }else if(input_bit == 11){ / return gr_complex(-3,-1); / }else if(input_bit == 12){ / return gr_complex(3,-3); / }else if(input_bit == 13){ / return gr_complex(1,-3); / }else if(input_bit == 14){ / return gr_complex(-1,-3); / }else if(input_bit == 15){ / return gr_complex(-3,-3); / }else{ / return gr_complex(0,0); / } / } / /* / * Our virtual destructor. / */ / constellation_mapping_4569_impl::~constellation_mapping_4569_impl() / { / } / int / constellation_mapping_4569_impl::work(int noutput_items, / gr_vector_const_void_star &input_items, / gr_vector_void_star &output_items) / { / auto in = static_cast<const input_type*>(input_items[0]); / auto out = static_cast<output_type*>(output_items[0]); / // constellation function dispatcher / gr_complex (*constellation_func[])(char) = {NULL, const_BPSK, const_QPSK, NULL, const_16QAM}; / float normal_factor[] = {0, 1, 1/sqrt(2), 0, 1/sqrt(10)}; / for(int i = 0; i < noutput_items; i++){ / if(_mod_bits_cnt == 1 || _mod_bits_cnt == 2 || _mod_bits_cnt == 4){ / out[i] = normal_factor[_mod_bits_cnt] * constellation_func[_mod_bits_cnt](in[i]); / }else{ / out[i] = gr_complex(0,0); / } / } / return noutput_items; / } / } /* namespace chris_module */ / } /* namespace gr */